## Slide 1
Blast Furnace Optimization
Approach Note
RIST-RAFT | HMT Prediction | EtaCO Forecasting

## Slide 2
JSW
Better Everyday
2
Agenda
Index
Executive summary and business context
Blast furnace process and operating challenge
Data landscape and preprocessing approach
Use case 1: RIST-RAFT methodology and outputs
Use case 2: HMT prediction approach
Use case 3: EtaCO forecasting approach
Integrated advisory framework
Roadmap and next steps

## Slide 3
JSW
Better Everyday
3
Executive Summary
Objective
Create one operator-focused blast-furnace advisory framework that combines physics, prediction and explainability to improve thermal stability, gas utilization and operating consistency.
Primary Use Cases
1. RIST-RAFT for blast and coke-rate guidance
2. HMT prediction for early temperature visibility
3. EtaCO forecasting for gas-utilization visibility
Business Intent
Help operators see risk earlier, understand the likely drivers, and evaluate practical responses on coke, PCI, oxygen enrichment, moisture, blast conditions and burden distribution.
The three use cases work together: RIST-RAFT explains the process, HMT predicts thermal drift, and EtaCO shows how efficiently the reducing gas is being used.

## Slide 4
JSW
Better Everyday
4
Business Context and Problem Statement
Why this matters
Hot metal temperature directly influences blast furnace productivity, fuel efficiency, slag handling, and downstream steelmaking quality.
Low HMT can create a chilling effect and make slag extraction difficult. High HMT can reduce efficiency and increase equipment deterioration risk.
The process is dynamically slow, which limits manual reaction time and makes forward-looking guidance valuable.
Operational challenges
Multiple tap holes with variable operating conditions
Maintenance can affect tap-hole behavior and measured temperatures
Gas anomalies, permeability issues and drainage inefficiencies influence furnace state
Low gas utilisation can indicate declining temperature trend
Liquid retention time must be minimized to avoid quality drift
Operators need early warning rather than after-the-fact diagnosis

## Slide 5
JSW
Better Everyday
5
Use Case Overview
Use Case 1
RIST-RAFT
First-principles / domain model used to estimate blast rate and coke rate under different operating conditions, with plant-level correction factors to improve practical fit.
Use Case 2
HMT Prediction
Data-driven model to predict hot metal temperature in advance, helping operators intervene on controllable levers before the process moves outside the desired range.
Use Case 3
EtaCO Forecasting
Forecasts gas-utilization efficiency from top-gas and operating data. It shows expected direction, confidence and key drivers so operators can investigate gas flow, permeability, burden and fuel settings before efficiency falls.
Together, the three use cases connect physics, thermal prediction and gas-efficiency insight in one advisory workflow.

## Slide 6
JSW
Better Everyday
6
Blast Furnace Process Understanding
Top Inputs
Iron carrier: iron ore, pellet and sinter
Carbon carrier: coke
Additives: limestone, dolomite and silica
These are charged from the top of the furnace at room temperature.
Bottom / Tuyere Inputs
Hot blast air is heated before oxygen addition.
Reducing gases and fuels are introduced through tuyere-side operation.
PCI, moisture and oxygen enrichment influence thermal balance and process kinetics.
Outputs
Tap-hole output: molten pig iron (liquid state) + slag + chemistry indicators such as C, Si, S, P and Mn.
Top output: reducing gases and by-products including CO, CO2, H2, H2O and N2.
The RIST framework models the blast furnace through conservation of mass and energy, linking operating inputs to thermal and material outputs.

## Slide 7
JSW
Better Everyday
7
Data Landscape and Operational Constraints
Available / Referenced Variables
Data_1 contains EtaCO, CO, CO₂, blast flow / pressure / temperature, O₂ enrichment, moisture, steam, RAFT, top-gas temperature, stockline, heat loss, CSR, tuyere velocity and pressure indicators.
Operational Notes
Measurements arrive at different frequencies and process responses are delayed. Time alignment, sensor-quality checks and lag-aware validation are required before modelling.
Observed Constraints
Recipe, Cast, HM and Slag sheets are available, but a reliable key or timestamp link to Data_1 is not yet confirmed. Phase 1 therefore uses Data_1 only.

## Slide 8
JSW
Better Everyday
8
Use Case 1: RIST-RAFT Methodology and Outputs
Model Logic
RIST-RAFT uses mass and enthalpy balancing equations to estimate blast furnace operating conditions. The model calculates blast rate and coke rate by solving the system iteratively from an initial assumption until the equations converge.
Core outputs
Calculated Blast Rate
Calculated Coke Rate
Interpretive operating pattern view: left-side behaviour indicates unfavourable condition, right-side behaviour indicates favourable condition
Guidance use
Model can be used to study different operating conditions by changing furnace parameters
Guidance is referenced as being generated every 30 minutes
Reverse RIST-RAFT logic can be used to study how controllable variables influence HMT

## Slide 9
JSW
Better Everyday
9
RIST-RAFT Calibration and Recommendation Logic
Calibration against plant
Model-predicted coke rate is expected to be lower than actual plant coke rate because plant losses exceed the losses explicitly represented in the simplified model.
Hence, plant-tested correction factors are used to reconcile the model with operating reality.
Blast Rate correction
Corrected value = Model predicted value / Correction factor
BF_1: 1.03
BF_2: 1.02
Coke Rate correction
Corrected value = Model predicted value / Correction factor
BF_1: 0.96
BF_2: 0.94
Recommendation scenarios
Reverse RIST-RAFT notes indicate that, under selected fixed conditions, the model can be used to explore how HMT responds to changes in PCI, moisture, oxygen enrichment and RAFT.
This becomes the bridge between descriptive physics and operator guidance.

## Slide 10
JSW
Better Everyday
10
Use Case 2: HMT Prediction
Use Case Objective
Predict hot metal temperature sufficiently in advance to help operators intervene before the process drifts outside the desired range.
Project notes indicate an intended prediction horizon of ~8 hours for decision support.
Data and Preparation
Data window: 1-Jan-2023 to 31-Mar-2024
Frequency: every 10 minutes
Rows: 62K+
Remaining after prep: ~48K
Cleaning includes shutdown filtering, removal of zero sensor values, moisture sanity checks, and outlier handling.
Modeling Notes
Feature candidates include hot blast flow, hot blast temperature, PCI, moisture, oxygen flow, ETA CO, permeability, blast air pressure, top gas temperature and HMT history.
RFR is noted as the strongest performer in the current material.

## Slide 11
JSW
Better Everyday
11
HMT Feature Logic and Temporal Averaging
The process is dynamically slow, so past data is weighted more heavily than current instant values.
Project notes reference both normal averaging and Gaussian-style temporal weighting.
The objective is to tune the historical window by variable to improve predictive fit.
Illustrative feature windows
Hot Blast Volume: 2 hours
ETA CO: 2 hours
Top gas temperature: 1 hour
Permeability: 1 hour
Hot Blast Temperature: 2 hours
Blast Pressure: 2 hours
PCI Rate: 2 hours
Oxygen Flow: 2 hours
Moisture: 1 hour
EDA notes
Box plots used for variable-wise outlier checks
Target variable filtered using HMT min/max range
Std scaler applied in -1 to +1 range
Performance judged through RMSE and MAE
Feature importance threshold referenced at > 0.05
Operational interpretation
A strong HMT signal can guide actions on PCI, moisture and coke-related settings.
The notes also connect HMT control to lower RAR and better blast furnace efficiency.

## Slide 12
JSW
Better Everyday
12
Use Case 3: EtaCO Forecasting
What EtaCO measures
ηCO = CO₂ / (CO + CO₂) × 100
It shows how much of the reducing CO gas completed useful reduction work.
Higher EtaCO: more CO converted to CO₂.
Lower EtaCO: more unused CO leaves the furnace.
Why forecast it
An early EtaCO forecast shows whether gas utilization is expected to improve or decline.
It supports:
• earlier investigation of gas-flow and permeability issues
• more stable reduction and fuel use
• clearer links between burden, blast and top-gas behaviour

## Slide 13
JSW
Better Everyday
13
EtaCO Data Readiness
Ready in Data_1
EtaCO target and timestamps; top-gas CO / CO₂; blast flow, pressure and temperature; oxygen, moisture, steam, RAFT, top-gas temperature, stockline, heat loss, CSR, tuyere velocity and pressure indicators.
Available but not linked
Recipe, Cast, HM and Slag sheets are available, but a reliable primary key or timestamp relationship to Data_1 is not yet confirmed. They are excluded from the initial baseline.
Useful upstream outputs
Burden: central coke ratio, ore/coke ratio, uniformity.
Permeability: index, resistance, pressure drop.
Gas flow: uniformity and stability.
These inputs remain optional / TBD until outputs are available.

## Slide 14
JSW
Better Everyday
14
EtaCO Model Plan: Build Value in Two Phases
Phase 1 | Baseline (1–2 weeks)
Use Data_1 only. Verify the EtaCO target and timestamps, clean the data, perform EDA, assess feature relevance, train an XGBoost regressor, test on future time blocks and explain results with SHAP.
Phase 2 | Forecasting (2–3 weeks)
Engineer process-delay features, train a GRU model, test agreed forecast horizons and tune for stability.
Why two phases
Phase 1 quickly proves feasibility. Phase 2 adds time-aware forecasting after the target, data quality and forecast horizon are validated.

## Slide 15
JSW
Better Everyday
15
EtaCO Depends on What Happened Earlier
Blast-furnace responses are delayed. Each input must be aligned to the time when it can influence EtaCO; otherwise the model may learn misleading relationships.
Typical lag windows
Blast temperature: 1–4 h
PCI: 1–2 h
Burden distribution: 4–8 h
Coke quality: 6–10 h
Sinter ratio: 5–8 h
Top pressure: minutes–1 h
Gas flow: immediate–1 h
Model training
Phase 1: XGBoost baseline
Phase 2: GRU time-series model
Use time-based train/test splits, rolling windows and configurable forecast horizons.
Explainability
SHAP summary and dependence plots
Local waterfall for each forecast
Actual vs predicted with confidence band
Error by time and operating regime

## Slide 16
JSW
Better Everyday
16
What the Operator Will Receive
Illustrative forecast
08:00 current EtaCO: 47%
Forecast for next 5 h: 43%
Direction: falling
Confidence: show prediction band
This is an example output format, not a plant result.
Why the model expects a drop
Possible drivers:
blast temperature at t–3 h
PCI at t–2 h
top pressure at t–1 h
How it is checked
Compare the forecast with actual EtaCO, track error, and review performance by operating regime.
Operator response
Review gas flow, permeability, burden distribution, blast temperature and PCI.
Evaluate actions only within approved operating constraints.
The model supports decisions; it does not automatically control the furnace.

## Slide 17
JSW
Better Everyday
17
Integrated Advisory Framework
Sense
Acquire Data_1 process, top-gas, pressure and thermal signals
Predict
Forecast HMT and EtaCO for the agreed horizon
Diagnose
Use SHAP, lag effects and RIST-RAFT physics
Advise
Present practical checks and controllable response options
Logic
If EtaCO is predicted to fall, check gas flow, permeability, burden distribution, blast temperature and PCI.
Cross-check the HMT forecast to distinguish gas-efficiency risk from thermal drift.
Use RIST-RAFT to evaluate blast-rate and coke-rate implications before action.

## Slide 18
JSW
Better Everyday
18
Decisions and Next Steps
Confirm Data_1 tag definitions, sampling frequency and sensor-quality rules.
Agree the EtaCO forecast horizon, alert threshold and acceptable error.
Validate the XGBoost baseline on a future time block.
Confirm whether Recipe, Cast, HM and Slag data can be linked reliably.
Start the lag-aware GRU phase after the baseline and horizon are approved.
Inputs to confirm
Permeability / burden / gas-flow model outputs, RIST-RAFT integration, operating constraints and plant sign-off criteria.

## Slide 19
JSW
Thank You