## Slide 1
Blast Furnace Optimization
Approach Note
RIST-RAFT | HMT Prediction | ETA CO2

## Slide 2
JSW
Better Everyday
2
Agenda
Index
Executive summary and business context
Blast furnace process and operating challenge
Data landscape and preprocessing approach
Use case 1: RIST-RAFT methodology and outputs
Use case 2: HMT prediction approach
Use case 3: ETA CO2
Integrated advisory framework
Roadmap and next steps

## Slide 3
JSW
Better Everyday
3
Executive Summary
Objective
Develop a blast furnace advisory framework that combines first-principles logic and predictive analytics to improve hot metal temperature visibility and support operator decision-making.
Primary Use Cases
1. RIST-RAFT for blast rate and coke rate guidance
2. HMT prediction for early temperature visibility
3. ETA CO2 as a gas-state linked supporting use case
Business Intent
Reduce hot metal temperature variability, improve operating consistency, and provide structured recommendations on controllable parameters such as coke, PCI, oxygen enrichment and blast-related conditions.
Blast furnace performance is strongly linked to thermal balance, gas behavior, burden descent and tap-hole operating conditions.

## Slide 4
JSW
Better Everyday
4
Business Context and Problem Statement
Why this matters
Hot metal temperature directly influences blast furnace productivity, fuel efficiency, slag handling, and downstream steelmaking quality.
Low HMT can create a chilling effect and make slag extraction difficult. High HMT can reduce efficiency and increase equipment deterioration risk.
The process is dynamically slow, which limits manual reaction time and makes forward-looking guidance valuable.
Operational challenges
Multiple tap holes with variable operating conditions
Maintenance can affect tap-hole behavior and measured temperatures
Gas anomalies, permeability issues and drainage inefficiencies influence furnace state
Low gas utilisation can indicate declining temperature trend
Liquid retention time must be minimized to avoid quality drift
Operators need early warning rather than after-the-fact diagnosis

## Slide 5
JSW
Better Everyday
5
Use Case Overview
Use Case 1
RIST-RAFT
First-principles / domain model used to estimate blast rate and coke rate under different operating conditions, with plant-level correction factors to improve practical fit.
Use Case 2
HMT Prediction
Data-driven model to predict hot metal temperature in advance, helping operators intervene on controllable levers before the process moves outside the desired range.
Use Case 3
ETA CO2
Supporting gas-linked use case based on available CO / CO2 measurements, intended to strengthen interpretation of furnace state and operating response.
Combined together, these use cases support a structured advisory layer for blast furnace operation.

## Slide 6
JSW
Better Everyday
6
Blast Furnace Process Understanding
Top Inputs
Iron carrier: iron ore, pellet and sinter
Carbon carrier: coke
Additives: limestone, dolomite and silica
These are charged from the top of the furnace at room temperature.
Bottom / Tuyere Inputs
Hot blast air is heated before oxygen addition.
Reducing gases and fuels are introduced through tuyere-side operation.
PCI, moisture and oxygen enrichment influence thermal balance and process kinetics.
Outputs
Tap-hole output: molten pig iron (liquid state) + slag + chemistry indicators such as C, Si, S, P and Mn.
Top output: reducing gases and by-products including CO, CO2, H2, H2O and N2.
The RIST framework models the blast furnace through conservation of mass and energy, linking operating inputs to thermal and material outputs.

## Slide 7
JSW
Better Everyday
7
Data Landscape and Operational Constraints
Available / Referenced Variables
Hot blast temperature
Blast rate / pressure
PCI rate
Moisture
Oxygen flow / enrichment
ETA CO / top gas
Permeability
Tap-hole temperatures
RAFT
BFG at tuyere openings
Operational Notes
16-17 tappings per day
2 to 4 temperature readings per tap
Tap remains open for ~2 hours
3-4 tap holes in operation
Typically, 2 tap holes open during daytime
Maintenance can leave one tap hole unavailable periodically
Observed Constraints
Gas analyser quality matters
Practically slag is not measured directly
Low gas utilisation may indicate temperature drop
Sensor cross-checking is required
Burden descent uniformity is observed via multiple sensors / radars

## Slide 8
JSW
Better Everyday
8
Use Case 1: RIST-RAFT Methodology and Outputs
Model Logic
RIST-RAFT uses mass and enthalpy balancing equations to estimate blast furnace operating conditions. The model calculates blast rate and coke rate by solving the system iteratively from an initial assumption until the equations converge.
Core outputs
Calculated Blast Rate
Calculated Coke Rate
Interpretive operating pattern view: left-side behaviour indicates unfavourable condition, right-side behaviour indicates favourable condition
Guidance use
Model can be used to study different operating conditions by changing furnace parameters
Guidance is referenced as being generated every 30 minutes
Reverse RIST-RAFT logic can be used to study how controllable variables influence HMT

## Slide 9
JSW
Better Everyday
9
RIST-RAFT Calibration and Recommendation Logic
Calibration against plant
Model-predicted coke rate is expected to be lower than actual plant coke rate because plant losses exceed the losses explicitly represented in the simplified model.
Hence, plant-tested correction factors are used to reconcile the model with operating reality.
Blast Rate correction
Corrected value = Model predicted value / Correction factor
BF_1: 1.03
BF_2: 1.02
Coke Rate correction
Corrected value = Model predicted value / Correction factor
BF_1: 0.96
BF_2: 0.94
Recommendation scenarios
Reverse RIST-RAFT notes indicate that, under selected fixed conditions, the model can be used to explore how HMT responds to changes in PCI, moisture, oxygen enrichment and RAFT.
This becomes the bridge between descriptive physics and operator guidance.

## Slide 10
JSW
Better Everyday
10
Use Case 2: HMT Prediction
Use Case Objective
Predict hot metal temperature sufficiently in advance to help operators intervene before the process drifts outside the desired range.
Project notes indicate an intended prediction horizon of ~8 hours for decision support.
Data and Preparation
Data window: 1-Jan-2023 to 31-Mar-2024
Frequency: every 10 minutes
Rows: 62K+
Remaining after prep: ~48K
Cleaning includes shutdown filtering, removal of zero sensor values, moisture sanity checks, and outlier handling.
Modeling Notes
Feature candidates include hot blast flow, hot blast temperature, PCI, moisture, oxygen flow, ETA CO, permeability, blast air pressure, top gas temperature and HMT history.
RFR is noted as the strongest performer in the current material.

## Slide 11
JSW
Better Everyday
11
HMT Feature Logic and Temporal Averaging
The process is dynamically slow, so past data is weighted more heavily than current instant values.
Project notes reference both normal averaging and Gaussian-style temporal weighting.
The objective is to tune the historical window by variable to improve predictive fit.
Illustrative feature windows
Hot Blast Volume: 2 hours
ETA CO: 2 hours
Top gas temperature: 1 hour
Permeability: 1 hour
Hot Blast Temperature: 2 hours
Blast Pressure: 2 hours
PCI Rate: 2 hours
Oxygen Flow: 2 hours
Moisture: 1 hour
EDA notes
Box plots used for variable-wise outlier checks
Target variable filtered using HMT min/max range
Std scaler applied in -1 to +1 range
Performance judged through RMSE and MAE
Feature importance threshold referenced at > 0.05
Operational interpretation
A strong HMT signal can guide actions on PCI, moisture and coke-related settings.
The notes also connect HMT control to lower RAR and better blast furnace efficiency.

## Slide 12
JSW
Better Everyday
12
Use Case 3: ETA CO2
Current understanding
-
Potential role
ETA CO2 can be positioned as a supporting gas-state intelligence layer.
-

## Slide 13
JSW
Better Everyday
13
Integrated Advisory Framework
Step 1
Acquire process, gas and tap-hole data
Step 2
Use HMT prediction to identify expected temperature drift
Step 3
Use RIST-RAFT logic to translate process state into blast rate / coke rate guidance
Step 4
Support operator response on controllable levers
Logic
If predicted HMT declines, investigate moisture, gas utilisation, PCI response and coke/blast settings.
If temperature is retained too long before tapping, quality drift such as silicon rise may occur.
ETA CO2 can strengthen interpretation of furnace gas behaviour in the same decision loop.

## Slide 14
JSW
Better Everyday
14
Next Steps
Validate and finalize the required tag list across blast, gas, tuyere and tap-hole measurements.
Confirm RIST-RAFT input/output definitions, correction-factor logic and operator-facing guidance scenarios.
Refine the HMT feature windows and retrain the strongest-performing model with validated plant data.
Develop the ETA CO2 section further once the supporting material and interpretation framework are confirmed.
Translate the technical logic into an operator-consumable advisory workflow and final management deck.
Open items
Research paper references, deeper ETA CO2 content, approved charts, and validation of plant-specific interpretation points.

## Slide 15
JSW
Thank You