## Slide 1
TEJAS
1
Agenda
01
Context, Problem definition, Scope, Baseline
02
Current vs Projected Performance
03
Conceptual Solution Design
04
Modeling methodology & theory
05
Architecture Design
06
Project Milestone & Timeline
07
Data Availability & Constraints
08
Team and Governance
09
Risks and Mitigation
Blast Furnace
HMT Prediction
Use Case
RIST-RAFT baseline + ML prediction to keep HMT in operating range and reduce RAR.

## Slide 2
TEJAS
2
Context, Problem definition, Scope, Baseline
Blast Furnace | HMT Prediction Use-Case
CONTEXT
Blast furnace converts iron ore into pig iron through reduction using coke. Efficiency and productivity are directly linked to Hot Metal Temperature (HMT).
PROBLEM
HMT response is slow (~8 hours) and both high / low temperatures impact performance, maintenance cost and slag extraction.
SCOPE
Build a RIST-RAFT baseline and ML prediction layer to guide operating changes for PCI, moisture, oxygen enrichment and coke rate.
Baseline Inputs / Manipulated Levers
Hot blast temperature
Hot blast volume
PCI rate
Moisture
Oxygen enrichment
Coke rate
Ore / coke ratio
Blast pressure
Target: keep HMT within ~1480-1500C and reduce Reducing Agent Ratio through timely operator guidance.

## Slide 3
TEJAS
3
Conceptual Solution Design
From furnace data to prescriptive operator guidance
Data Source Layer
Historian / DCS
Lab quality data
Manual logs & recipes
Data Prep Layer
Shutdown filtering
Zero / invalid sensor filtering
Temporal averaging
Model Layer
RIST-RAFT baseline
HMT prediction ML
Reverse recommendation logic
Optimization Layer
PCI / moisture suggestions
Coke & blast-rate checks
Constraint handling
Guidance Layer
30-min recommendations
Operator action points
HMT range monitoring
Expected operating rhythm
Predict HMT well in advance (~8-hour response window) using historical and high-frequency signals.
Use reverse RIST-RAFT recommendations to control PCI, moisture and coke-rate levers.
Model output is guidance, not automation: plant team validates suggestions before operational changes.